## Slide 1: Quiz
Simplify the following function and calculate the gate input cost with and without Not gate for the original F. (6 pts)
For the following function, answer questions:
  Optimize F in SOP form; (4 pts)
  Find all prime implicants and essential prime implicants; (6 pts)
  Optimize F in POS form; (4 pts)

## Slide 2: Answer
1. Simply the function (6 points)
(G=15)
(GN=18)
2.
SOP. or
Primes: , ,
essentials: , ,
POS.
1 |  |  | 1
 | 1 | 1 | 1
1 |  |  | 1

## Slide 3: Quiz
Given the following logic circuits implemented with three 2-to-1 multiplexors and inputs A, B and C, please find the logic expressions of X, Y and F in its SOM form.
Design a circuit with a 8-to-1 multiplexer to generate a odd-parity bit for binary code (b3,b2,b1,b0). Write down the truth table, and the circuit.

## Slide 4: Quiz
Design a circuit with a 8-to-1 multiplexer to decide whether a 4-bits binary number can be divided by 4, output 1 if yes, otherwise output 0. Write down the truth table, logic function and the circuit.
Design a 7-segment display using a 22 x 7 ROM. There is 2 Inputs: A1 and A0 and 7 Outputs: a ~ g; if a ~ g = 1, LED light is on, and if a ~ g = 0, the light is off. You only need to display 0, 1, 2, 3 as follows. Draw the circuit design on the ROM plane.

## Slide 5: Quiz
Design a circuit which implements 4-bit incrementing/decrementing use a 4-bits full adder: when the input S=0, the circuit performs increment, when S=1, the circuit performs decrement.
Design a counter, when the control signal C=1, the counting sequence is 000100110111011000; when C=0, the counting sequence is 000100110010011000. Please write the state diagram, state table, next state function, output function and draw the circuit.

## Slide 6: Quiz
Given a circuit in figure (a):
  write down its state table and state diagram.
  Assume the initial state is 0 and input X waveform is shown in (b), write down the waveform of Q and Z.
Design a counter, when the control signal C=1, the counting sequence is 000100110111011000; when C=0, the counting sequence is 000100110010011000. Please write the state diagram, state table, next state function, output function and draw the circuit.

## Slide 7: Quiz 4
Use two 4-bit synchronous binary counters and logic gates to implement a 2-bits date counter that counts from decimal “01” through decimal “31”. (and “28”)
Give two register transfer operations (R1 unchanged except for the following cases):
C1: R1R1 + R2
(~C1)C2: R1R1 - 1
Use two 4-bits registers, one 4-bit adder, and other necessary gates to implement the above operations.